## Slide 1: Vehicle to Infrastructure Platform Concept 7 July 2022

## Slide 2: V2X Connected Intersection
RSU
ATC
TMC
TMC – Traffic Management Center
ATC – Advanced Traffic Controller
RSU – V2X Road Side Unit
OBU – V2X On Board Unit
TMC connected to city wide ATCs and RSUs
TMC configures RSUs with intersection MAP and Traveler Information Messages (TIMs) to broadcast.
ATC controls traffic light signal phase and timing (SPaT) and communicates the SPaT to RSU
RSU broadcasts SPaT, MAP, and TIMs to nearby vehicles (up to 1 km range)
OBU

## Slide 3: 5G Connected Intersection
ATC
TMC
TMC configures SGW with intersection MAP and TIM messages
ATC communicates real time SPaT to Smart Gateway (SGW)
SGW communicates SPaT to the Cloud through the TMC
Cloud offers to communicate (over 5G) SPaT, MAP, and TIMs to vehicles within 1 km of the vRSU
Vehicle processes the offers and accepts to receives the data required
vRSU – Virtual Road Side Unit
Bitbrew
vRSU
5G
Smart GW

## Slide 4: 5G Connected Intersection
ATC
TMC configures SGW with intersection MAP and TIM messages
ATC communicates real time SPaT to Smart Gateway (SGW)
SGW communicates SPaT to the Cloud using onboard LTE / 5G.
Cloud offers to communicate (over 5G) SPaT, MAP, and TIMs to vehicles within 1 km of the vRSU
Vehicle processes the offers and accepts to receives the data required
vRSU – Virtual Road Side Unit
Bitbrew
vRSU
5G
Smart GW
5G

## Slide 5: Hybrid Connected Intersection
RSU and vRSU simultaneously broadcast / communicate SPaT, MAP, and TIMs to vehicle OBUs in proximity to the relevant intersection
Information follows the same format setup by the V2X standards
Vehicle OBU / 5G processing of the intersection information for V2I applications remains the same, independent of the source
ATC
TMC
5G / OBU
Smart GW
5G / RSU
or use RSU
Fiber or 5G to cloud
Bitbrew
vRSU

## Slide 6: V2I Platform Goals
Efficiency of platform to scale high numbers of vRSU and vehicle device instances (USA 300k intersections and 250M vehicles)
Low latency of infrastructure data (i.e. SPaT, others) to vehicles
Platform and vehicle device communication APIs for standardization of interoperability with other platforms or vehicle devices
Data messaging common to existing V2X standards (J2735) where possible
Flexibility to support various vehicle devices (OBU, TCU, Datalogger, mobile phone, etc.)
Flexibility to support various infrastructure equipment (SGW, RSU, ATC, others) for edge communication
Flexibility to push / pull data from other platforms

## Slide 7: V2I Platform Components
ATC/TMC Configuration
SGW/RSU Device Management, Configuration & Security Authentication
vRSU Configuration
UserClient Management, Configuration & Security Authentication
  UserClient can be V2X_Vehicle (or) Authorized_IoT_Device [Pedestrian with Cell Phone]
UserClient Location Upload to Platform
  J2735_SnapShot for V2X_Vehicle. Frequency of Upload could be proportional to Vehicle Speed.
  List of PSIDs that the UserClient can support to receive and process
Platform Geo-Fencing logic
  To Filter only relevant vRSU(s) based on received Location
  Platform to stream J2735 Messages as per the requested PSIDs to UserClient
Platform forward vRSU(s) Data to UserClient
  MAP, SPaT, TIM, PSM, RTCM, etc.
UserClient Applications
  In-V2X_Vehicle can provide Red-Light Violation Warning Annunciation using MAP & SPaT Data received
  In-V2X_Vehicle can place Traffic Signal Priority / Preemption to ATC through Platform / SGW
  Pedestrian with Cell Phone (Authorized_IoT_Device) can report Traffic Incident

## Slide 8: V2I Platform Components (contd.)
Payment / subscription services [FUTURE]
  Tolling
vRSU Applications & Advisories Download to Vehicles [FUTURE]
  Road Weather Applications (Cloud Based ICE Warning)

## Slide 9: Concept Diagram
Bitbrew
Smart GW
RoadSideClient #1
Smart GW
Smart GW
RoadSideClient #2
RoadSideClient #3
MY POSITION
DATA STREAM
vRSU #1
MY “NEW” POSITION
RoadSideClient #4
Construction Zone TIM #1
RoadSideClient #5
Construction Zone TIM #2
DATA STREAM
vRSU #2 + vRSU #3

## Slide 10: V2X Platform Data Parameters
Vehicle position to Cloud:
less than 50 kph [every 5s]
greater than 50 kph [every 1s]
vRSUs Geofence distance threshold:
less than 50 kph [300 m radius]
greater than 50 kph [1000 m radius]
MAP and TIM messages [1x only]
SPaT [1x then repeat on phase change]
Note: Intention is to keep data content low for cellular cost efficiency.

## Slide 11: MQTT Implementation Guide for V2X_Platform Concept
This presentation covers MQTT requirements of the service lane Dongle app
Topics Tree to be used by MQTT Client(s)
MQTT Payload definition
MQTT Configuration options

## Slide 12: Topics Tree
{Payload Directionality} /{ID}/{Message Category}/
1st level topic : Payload Directionality
  RoadSideClientToPlatform – Used when SGW / RSU is publishing data to the Platform
  PlatformToUserClient – Used when UserClient subscribes to Data from the Platform
  UserClientToPlatform – Used when UserClient publishes Data to the Platform
2nd level topic : ID
  RSC_id – Unique Identifier for each RoadSide Client (SGW, RSU, Road Construction Worker, etc. )
  UC_id – Unique Identifier for each User Client
3rd level topic : Message Category
  MAP – Used when RSC wants to publish MAP Data to Platform
  SPaT – Used when RSC wants to publish SPaT Data to Platform
  TIM – Used when RSC wants to publish TIM Data to Platform
  SubscribedPayload – Used when UC subscribes to data.
  UserClientUpload – Used when UC subscribes to data.
3rd Level Topic could be expanded in the future to accommodate for more messages like: PSM, RTCM, etc.

## Slide 13: RoadSideClient -> Platform
MQTT Broker
Platform
RoadSide
Client #1
PUBLISH
/RoadSideClientToPlatform/RSC_id/MAP/Payload
/RoadSideClientToPlatform/*
SUBSCRIBE
PUBLISH
/RoadSideClientToPlatform/RSC_id/MAP/Payload
/RoadSideClientToPlatform/RSC_id/SPaT/Payload
RoadSide
Client #2
/RoadSideClientToPlatform/RSC_id/SPaT/Payload
RoadSideClient -> Platform [PUBLISH] | 
topicName | /RoadSideClientToPlatform/RSC_id/MAP
qos | 1
retaingFlag | false
payload | ASN.1 Encoded UPER Payload of MAP (or) SPaT (or) TIM Message
dupFlag | false
xyz – To be finalized
xyz – Could be MAP, SPaT (or) TIM

## Slide 14: UserClient -> Platform
MQTT Broker
Platform
UserClient #1
PUBLISH
/UserClientToPlatform/UC_id/UserClientUpload/Payload
/UserClientToPlatform/*
SUBSCRIBE
UserClient #2
PUBLISH
/UserClientToPlatform/UC_id/UserClientUpload/Payload
UserClient -> Platform [PUBLISH] | 
topicName | /UserClientToPlatform/UC_id/UserClientUpload
qos | 1
retaingFlag | false
payload | ASN.1 Encoded UPER Payload of UserClientUpload Message
dupFlag | false
xyz – To be finalized

## Slide 15: Platform -> UserClient
Platform
UserClient #1
/PlatformToUserClient/UC_id/SubscribedPayload
/PlatformToUserClient/UC_id/SubscribedPayload
SUBSCRIBE
UserClient #2
PUBLISH
/PlatformToUserClient/UC_id/SubscribedPayload
PUBLISH
MQTT Broker
/PlatformToUserClient/UC_id/SubscribedPayload
SUBSCRIBE
Platform -> UserClient [PUBLISH] | 
topicName | /PlatformToUserClient/UC_id/SubscribedPayload
qos | 1
retaingFlag | false
payload | ASN.1 Encoded UPER Payload of MAP (or) SPaT (or) TIM Message from all RSCs that satisfy the Geo-Fencing Logic
dupFlag | false
xyz – To be finalized

## Slide 16: Sequence Diagram

## Slide 17: MQTT Payload definition [UserClientUpload]
UserClientUpload ::= SEQUENCE {
positionUpload PositionUpload,
extendedUpload ExtendedUpload OPTIONAL,
supportedServicesUpload SEQUENCE (SIZE(1..32)) OF Psid OPTIONAL,
...
}
PositionUpload
  Contains information about geo-location of the UserClient
ExtendedUpload
  OPTIONAL
  UserClient can upload extended information to Platform that cannot be covered in positionUpload
  Example : SRM, RWM, etc
SEQUENCE of Psid
  OPTIONAL
  UserClient can upload list of PSIDs the UserClient is interested to receive from Platform
  To be uploaded once per ignition cycle. Can be ignored afterwards.
  Example:
    0x20-40-97 = MAP Distribution
    0x82 = Intersection Safety Awareness (SPaT)
PSIDs from https://standards.ieee.org/products-programs/regauth/psid/public/

## Slide 18: MQTT Payload definition [PositionUpload]
PositionUpload ::= CHOICE {
vehiclePositionUpload SEQUENCE (SIZE(1..32)) OF SnapShot,
nonVehiclePositionUpload SnapShot,
...
}
vehiclePositionUpload => SEQUENCE of SnapShot
  BSM has no sense of exact UTC Minute, Hour, Day, etc. It only has Dsecond of the current minute.
  SnapShot has full UTC Date + TimeStamp.
  Snapshot also has PathHistory + PathPrediction.
  This is useful for Platform to accept / reject packets with high latency.
  vehiclePositionUpload is given the capability to upload sequence of Snapshots since it might have that processing power and capability.
nonVehiclePositionUpload => SnapShot
  For a non-vehicle user, it might be possible to upload only one snapShot of data.
  So, reducing its capability to a single SnapShot and not a sequence of them.

## Slide 19: MQTT Payload definition [ExtendedUpload]
ExtendedUpload ::= CHOICE {
priorityRequestUpload SignalRequestMessage,
preemptionRequestUpload SignalRequestMessage,
...
}
priorityRequestUpload => SignalRequestMessage
  Based on vehicle role, UserClient can place a Priority Signal Request Message to Platform
  Example: SnowPlows, TransitBuses, etc.
  SignalRequestMessage->SignalRequestList has the capability to hold multiple requests for different intersections
preemptionRequestUpload => SignalRequestMessage
  Based on vehicle role, UserClient can place a Preemption Signal Request Message to Platform
  Example: PoliceCars, FireTrucks, etc.
  SignalRequestMessage->SignalRequestList has the capability to hold multiple requests for different intersections

## Slide 20: TMC Configuration
If traffic is going to be routed through TMC,
Establish outbound path for SGW/RSU to Platform (IPv4 and IPv6)
Work with relevant DOT to Whitelist the Platform in TMC
Produce Security requirements to authenticate and verify identity of each SGW/RSU talking to Platform

## Slide 21: SGW/RSU Device Management, Configuration & Security
Geo-Location Configuration
Network configuration to communicate with ATC for SPaT
Security Enrollment to authenticate Identity of SGW/RSU communicating to Platform.
  Use HTTPS with TLS to implement:
    Client Authentication
    Encrypted Data download from Platform.
SGW should be able to take MAP Message as an Input Configuration
  MAP Message is a UPER Encoded Hex Stream of Bytes as per J2735.
  IntersectionID derived from MAP Message
  SGW will need to have to capability to decode Encoded Hex Payload.
Should support multiple ATC Supplier Data Formats
  Trafficware, D4, Econolite, Siemens, McCain, RSU 4.1 Active Message, etc.
OTA device updates to SGW/RSU
SoH monitoring
For Signal Priority / Preemption [FUTURE]
  SmartGW should have a configurable Lookup Tables.
  Phase Number | Priority Number in TC
  Phase Number | Preemption Number in TC

## Slide 22: UserClient Device Management, Configuration & Security
Security Enrollment to authenticate Identity of SGW/RSU communicating to Platform.
  Use HTTPS with TLS to implement:
    Client Authentication
    Encrypted Data download from Platform.
OTA device updates to SGW/RSU
SoH monitoring

## Slide 23: vRSU Configuration
Each VGW/RSU connecting to Platform is a vRSU Node on the Platform
Each vRSU node on the network should be able to offer multiple services
  MAP Distribution
  SPaT Distribution
  RTCM Distribution
  Pedestrian Detection / PSM Distribution
  Signal Priority / Preemption

## Slide 24: UserClient Data Upload
If UserClient is a V2X_Vehicle,
Uploads the below message to Platform:
  UserClientPlatformMessage
    positionUpload
      vehiclePositionUpload
Frequency of Upload should be proportional to Vehicle Speed.
First time a UserClient connects to platform, “supportedServicesUpload” should be populated
If UserClient is an Authorized_IoT_Device [Pedestrian with Cell Phone],
Uploads the below message to Platform:
  UserClientPlatformMessage
    positionUpload
      nonVehiclePositionUpload
      First time a UserClient connects to platform, “supportedServicesUpload” should be populated

## Slide 25: Platform Geo-fencing relevant vRSUs & Data Stream
Using the Geo-Location, Speed and Heading from the uploaded data from UserClient,
  Platform to apply a Geofence around the received Location data and pick out the relevant vRSU Nodes.
  Platform to also parse the requested PSIDs from the UserClient
  Platform to stream all applicable PSID data from the list of relevant vRSUs to UserClient
The Geo-Fencing Logic will have to be dynamic based on the proximity of vRSUs to each other in an area.
  Very dense areas (Example: Manhattan) the applicable vRSUs will be:
    2 Ahead in travel direction
    1 Left Ahead
    1 Right Ahead
    1 Behind
  Mild dense areas (Example: Novi) the applicable vRSUs will be:
    2 Ahead in travel direction
    1 Behind
  Sparse Areas (Example: Highways) the applicable vRSUs will be:
    1 Ahead in travel direction

## Slide 26: UserClient Applications and Advisories Annunciation to Driver
Same as V2X OBU, all platform communicated data evaluated along with vehicle path to determine driver advisories and warnings

## Slide 27: Payment / subscription services
Method to pay for platform services during enrollment of vehicle devices.
May have to pay the DOTs for access to the ATC data

## Slide 28: vRSU Applications & Advisories Download to Vehicles
Any platform vRSU based applications data or advisories
Intersection sensor detection of environment:
Pedestrian presence
Vulnerable road user presence
Vehicle presence (especially intersecting path vehicles)

## Slide 29: To do List
Produce Security Requirements to implement:
  UserClient Identity Authentication
  vRSU Identity Authentication
Define Periodicity of Messages being published to Platform
  Investigate Scope for reducing periodicity